## Slide 1: 数字系统设计 CMOS 门
刘 鹏
浙江大学
信息与电子工程学院
liupeng@zju.edu.cn

## Slide 2: MOS管结构和符号
MOS: Metal-Oxide-Semiconductor Field-Effect Transistor
VGS(th)称为MOS管的开启电压
VGS=0漏极和源极之间相当于两个PN结背向地串联，所以D-S间不导通. iD=0

## Slide 3
CMOS 反相器
NMOS
PMOS
柵极相连做输入端
漏极相连做输出端
衬底与漏源间的PN结始终处于反偏，NMOS管的衬底总是接到电路的最低电位，PMOS管的衬底总是接到电路的最高电位
VDD＞VGS(th)N+|VGS(th)P|， VGS(th)N--NMOS的开启电压
VGS(th)P--PMOS的开启电压
VGS(th)N=|VGS(th)P|
工作原理：
1、输入为低电平VIL = 0V时
VGS1＜VGS(th)N
T1管截止；
|VGS2| ＞ |VGS(th)P|
电路中电流近似为零（忽略T1的截止漏电流）,VDD主要降落在T1上，输出为高电平VOH≈VDD
T2导通
2、输入为高电平VIH = VDD时，T1通T2止，VDD主要降在T2上，输出为低电平VOL≈0V。
实现逻辑“非”功能

## Slide 4
电压传输特性
0.5VDD
Vo
VI
VDD
VGS(th)n
VGS(th)p 
VDD
1/2VDD
A
B
C
D
E
F
电流传输特性
iD
VI
VGS(th)n
VGS(th)p 
VDD
1/2VDD
A
B
C
D
E
F
电压传输特性和电流传输特性
T2
T1
VO
VI
VDD
iD
VSS
T1截止、T2非饱和；所以 iD=0
T1饱和、T2非饱和； T1 、 T2均导通，所以产生 iD电流。
T1、T2均饱和导通； 此时非门为反向放大器，产生较大iD电流。
T1非饱和导通、
T2饱和导通。
T1非饱和、T2截止；所以 iD=0

## Slide 5
CMOS反相器的输出特性
T2
VSS
VIH=VDD
VDD
RL
VOL
（1）输出低电平
低电平导通电阻：ROL≤ 1k Ω
最大低电平输出电流IOL
（以4069为例）
0.36mA（ VDD =5V ）
0.9mA （ VDD =10V）
2.4mA （ VDD =15V）
电阻负载能力差

## Slide 6
T1
VOH
VIL=0
VDD
IOH
RL
（2）输出高电平
高电平导通电阻：ROH≤ 1k Ω
最大高电平输出电流IOH ： （以4069为例）
-0.51mA（ VDD =5V）
-1.3mA （ VDD =10V）
-3.4mA （ VDD =15V）
（3）扇出系数：
N>50
注意：CMOS门（ VDD =5V）可驱动一个TTL门
驱动能力强
因为，CMOS门的输入阻抗为∞，但考虑到分布参数，一般取50
CMOS反相器的输出特性

## Slide 7
传输延时原因：
vI
vO
O
O
t
t
50%
50%
tPHL
tPLH
二、动态功耗
分布参数
负载电容
MOS管开关延时
f
Pc
CMOS反向器传输延时时间

## Slide 8
二输入“与非”门电路结构如图
当A和B为高电平时:
1
两个串联的NMOS T1、T2
通
通
止
止
0
0
1
通
止
1
止
当A和B有一个或一个以上为低电平时:
电路输出高电平
输出低电平
 电路实现“与非”逻辑功能
与非门逻辑功能的CMOS门电路
两个并联的PMOS管T3、T4
每个输入端与一 个 NMOS管和一个PMOS管的栅极相连
通
1

## Slide 9
T3
T1
T2
T4
A
B
Y
VDD
二输入“或非”门电路结构如图
当A和B为低电平时:
1
两个串联的PMOS管T1、T3
两个并联的NMOS T1、T2
通
止
0
当A和B有一个或一个以上为高电平时:
电路输出低电平
输出高电平
 电路实现“或非”逻辑功能
0
通
止
1
0
止
通
0
或非门逻辑功能的CMOS门电路

## Slide 10: 漏极开路门电路（OD门）
外接上拉负载电阻
1.电路组成
2.逻辑符号
&
A
B
Y
必须外接负载电阻RL ，才能实现：
3.原理
A
Y
B
VDD2
RL
&
1
VDD1
CD40107
4.应用
与OC门一样，可做“线与”、“电平变换”等作用。
漏极开路

## Slide 11
CMOS传输门和双向开关
1.电路结构：
2.工作条件：
VI /Vo
VDD
Vo/VI
T1
T2
VSS
VI
VDD
Vo
RL

## Slide 12
CMOS传输门和双向开关原理
（1）
时
VI
VDD
Vo
RL
T1
T2
S2
S1
D2
D1
都截止

## Slide 13
a. T1非饱和导通条件
（VDS< VGS-VGS(th)N）：
VI
VDD
Vo
RL
T1
T2
S2
S1
D2
D1
假设T1非饱和导通，
∵ RL>> RON∴ Vo≈ VI 则有：
0 < (VDD - VI)- VGS(th)N
VI
VDD
0
VGS(th)P
VGS(th)N
T1导通
VDS = VI – V0 ≈0
VGS = VDD – V0
≈ VDD – VI
T1非饱和导通条件:
同理，T2非饱和导通条件:
T2导通
由于，CMOS器件的源极和栅极在结构上是对称，所以传输门是双向的
T1 、 T2至少有一个非饱和导通，
所以， 时，传输门导通

## Slide 14
Vo/VI
TG
VI /Vo
CMOS传输门
门控制信号
输入/输出
输出/输入
特别提示：传输门相当于一个理想的开关，且是一个双向开关,可传输模似信号。
C=0，开关断开； C=1，开关接通。
主要应用
双向模拟开关，
数据选择器（可传输模拟信号）

## Slide 15
CMOS三态门
1.电路组成
2.逻辑符号
Y
VDD
T1
T2
T'1
A
1
T'2
3.原理：
4.三态门的应用
主要应用：
总线逻辑
双向传输
A
Y

## Slide 16: Transistor-level Logic Circuits (INV)
Inverter (NOT gate):
Vdd
Gnd
Vdd
Gnd
0 volts
in
out
3 volts
what is the relationship between in and out?

## Slide 17: Logical Values
Threshold
  Logical 1 (true) : V > Vdd –V th
  Logical 0 (false) : V < Vth
Noise margin?
V
+3
0
Logic 1
Logic 0
Vout
+3
0
Logic 0 Input Voltage
Logic 1 Input Voltage
Vin
+5
F
in
out
T
T
F
not( out, in)

## Slide 18: Computing with Switches
AND
OR
Z  A and B
Z  A or B
A
B
A
B
Compose switches into more complex (Boolean) functions:
Two fundamental structures: series (AND) and parallel (OR)

## Slide 19: Transistor-level Logic Circuits - NAND
Inverter (NOT gate):
NAND gate
Logic Function:
  out = 0 iff both a AND b = 1 therefore out = (ab)’
  pFET network and nFET network are duals of one another.
How about AND gate?
a b out
0 0 1
0 1 1
1 0 1
1 1 0
nand (out, a, b)

## Slide 20: Transistor-level Logic Circuits
nFET is used only to pass logic zero.
pFet is used only to pass logic one.
For example, NAND gate:
Simple rule for wiring up MOSFETs:
Note: This rule is sometimes violated
by expert designers under special conditions.

## Slide 21: Transistor-level Logic Circuits - NOR
NAND gate
NOR gate
Function:
  out = 0 iff both a OR b = 1 therefore out = (a+b)’
  Again pFET network and nFET network are duals of one another.
  Other more complex functions are possible. Ex: out = (a+bc)’
a b out
0 0 1
0 1 0
1 0 0
1 1 0
nor (out, a, b)

## Slide 22: Transmission Gate
Transmission gates are the way to build “switches” in CMOS.
Both transistor types are needed:
  nFET to pass zeros.
  pFET to pass ones.
The transmission gate is bi-directional (unlike logic gates and tri-state buffers).
Functionally it is similar to the tri-state buffer, but does not connect to Vdd and GND, so must be combined with logic gates or buffers.

## Slide 23: Transistor-level Logic Circuits
Transistor circuit for inverting tri-state buffer:
“high impedance” (output disconnected)
Variations
Tri-state Buffer
“transmission gate”
Inverting buffer
Inverted enable
Tri-state buffers are used when multiple circuits all connect to a common bus.
Only one circuit at a time is allowed to drive the bus. All others “disconnect”.

## Slide 24: Transistor-level Logic Circuits - MUX
Multiplexor
If s=1 then c=a else c=b
Transistor Circuit for inverting multiplexor:

## Slide 25: Unused Inputs
CMOS inputs should be never be left disconnected. All CMOS inputs must be tied either to a fixed voltage level (0V or VDD) or to another input.
This rule applies even to the inputs of extra unused logic gates on a chip.
An unconnected CMOS input is susceptible to noise and static charges that could easily bias both the P-channel and the N-channel MOSFETs in the conductive state, resulting in increased power dissipation and possible overheating.